## Slide 1: Geometric Gradients
Geometric gradients change by the same percentage each period
0
1
2
3
n
A1
A 1(1+g)1
4
A 1(1+g)2
A 1(1+g)n-1
Pg = ?
There are no tables for geometric factors
Use following equation for g ≠ i:
Pg = A1{1- [(1+g)/(1+i)]n}/(i-g)
where: A1 = cash flow in period 1
g = rate of increase
If g = i, Pg = A1n/(1+i)
Note: If g is negative, change signs in front of both g values
Cash flow diagram for present worth
of geometric gradient
Note: g starts between
periods 1 and 2

## Slide 2: Example: Geometric Gradient
Find the present worth of $1,000 in year 1 and amounts increasing by 7% per year through year 10. Use an interest rate of 12% per year.
(a) $5,670 (b) $7,333 (c) $12,670 (d) $13,550
0
1
2
3
10
1000
1070
4
1145
1838
Pg = ?
Solution:
Pg = 1000[1-(1+0.07/1+0.12)10]/(0.12-0.07)
= $7,333
Answer is ?
g = 7%
i = 12%
To find A, multiply Pg by (A/P,12%,10)

## Slide 3: Unknown Interest Rate i
Unknown interest rate problems involve solving for i,
given n and 2 other values (P, F, or A)
(Usually requires a trial and error solution or interpolation in interest tables)
A contractor purchased equipment for $60,000 which provided income of $16,000 per year for 10 years. The annual rate of return of the investment was closest to:
(a) 15% (b) 18% (c) 20% (d) 23%
Can use either the P/A or A/P factor. Using A/P:
Solution:
60,000(A/P,i%,10) = 16,000
(A/P,i%,10) = 0.26667
From A/P column at n = 10 in the interest tables, i is between 22% and 24%
Answer is (d)
Procedure: Set up equation with all symbols involved and solve for i

## Slide 4: Unknown Recovery Period n
Unknown recovery period problems involve solving for n,
given i and 2 other values (P, F, or A)
(Like interest rate problems, they usually require a trial & error solution or interpolation in interest tables)
Procedure: Set up equation with all symbols involved and solve for n
A contractor purchased equipment for $60,000 that provided income of $8,000
per year. At an interest rate of 10% per year, the length of time required to recover
the investment was closest to:
(a) 10 years (b) 12 years (c) 15 years (d) 18 years
Can use either the P/A or A/P factor. Using A/P:
Solution:
60,000(A/P,10%,n) = 8,000
(A/P,10%,n) = 0.13333
From A/P column in i = 10% interest tables, n is between 14 and 15 years
Answer is (c)

## Slide 5: Summary of Important Points
In P/A and A/P factors, P is one period ahead of first A
In F/A and A/F factors, F is in same period as last A
To find untabulated factor values, best way is to use formula or spreadsheet
For arithmetic gradients, gradient G starts between periods 1 and 2
Arithmetic gradients have 2 parts, base amount (year 1) and gradient amount
For geometric gradients, gradient g starts been periods 1 and 2
In geometric gradient formula, A1 is amount in period 1
To find unknown i or n, set up equation involving all terms and solve for i or n

## Slide 6: Shifted Series

## Slide 7: Shifted Uniform Series
A shifted uniform series starts at a time other than period 1
0
1
2
3
4
5
A = Given
PA = ?
The cash flow diagram below is an example of a shifted series
Series starts in period 2, not period 1
Shifted series usually
require the use of
multiple factors
Remember: When using P/A or A/P factor, PA is always one year ahead
of first A
When using F/A or A/F factor, FA is in same year as last A
FA = ?

## Slide 8: Example Using P/A Factor: Shifted Uniform Series
P0 = ?
A = $10,000
0 1 2 3 4 5 6
i = 10%
The present worth of the cash flow shown below at i = 10% is:
(a) $25,304 (b) $29,562 (c) $34,462 (d) $37,908
Solution: (1) Use P/A factor with n = 5 (for 5 arrows) to get P1 in year 1
(2) Use P/F factor with n = 1 to move P1 back for P0 in year 0
P0 = P1(P/F,10%,1) = A(P/A,10%,5)(P/F,10%,1) = 10,000(3.7908)(0.9091) = $34,462
0 1 2 3 4 5
P1 = ?
Actual year
Series year

## Slide 9
How much money would be available in year 10 if $8000 is deposited each year in years 3 through 10 at an interest rate of 10% per year?
0 1 2 3 4 5 6 7 8 9 10
FA = ?
A = $8000
i = 10%
Solution:
Re-number diagram to determine n = 8 (number of arrows)
0 1 2 3 4 5 6 7 8
Cash flow diagram is:
FA = 8000(F/A,10%,8)
= 8000(11.4359)
= $91,487
Example Using F/A Factor: Shifted Uniform Series
Actual year
Series year

## Slide 10: Shifted Series and Random Single Amounts
For cash flows that include uniform series and randomly placed single amounts:
Uniform series procedures are applied to the series amounts
Single amount formulas are applied to the one-time cash flows
The resulting values are then combined per the problem statement
The following slides illustrate the procedure

## Slide 11: Example: Series and Random Single Amounts
Find the present worth in year 0 for the cash flows
shown using an interest rate of 10% per year.
0 1 2 3 4 5 6 7 8 9 10
PT = ?
A = $5000
i = 10%
First, re-number cash flow diagram to get n for uniform series: n = 8
$2000
0 1 2 3 4 5 6 7 8 9 10
PT = ?
A = $5000
i = 10%
$2000
0 1 2 3 4 5 6 7 8
Solution:
Actual year
Series year

## Slide 12: Example: Series and Random Single Amounts
A = $5000
i = 10%
0 1 2 3 4 5 6 7 8
Actual year
Series year
0 1 2 3 4 5 6 7 8 9 10
$2000
Use P/A to get PA in year 2: PA = 5000(P/A,10%,8) = 5000(5.3349) = $26,675
Move PA back to year 0 using P/F: P0 = 26,675(P/F,10%,2) = 26,675(0.8264) = $22,044
Move $2000 single amount back to year 0: P2000 = 2000(P/F,10%,8) = 2000(0.4665) = $933
Now, add P0 and P2000 to get PT: PT = 22,044 + 933 = $22,977
PT = ?
PA

## Slide 13
Example Worked a Different Way
(Using F/A instead of P/A for uniform series)
0 1 2 3 4 5 6 7 8 9 10
PT = ?
A = $5000
i = 10%
$2000
0 1 2 3 4 5 6 7 8
The same re-numbered diagram from the previous slide is used
Solution:
Use F/A to get FA in actual year 10: FA = 5000(F/A,10%,8) = 5000(11.4359) = $57,180
Move $2000 single amount back to year 0: P2000 = 2000(P/F,10%,8) = 2000(0.4665) = $933
Now, add two P values to get PT: PT = 22,043 + 933 = $22,976
Same as before
Move FA back to year 0 using P/F: P0 = 57,180(P/F,10%,10) = 57,180(0.3855) = $22,043
As shown, there are usually multiple ways to work equivalency problems
FA = ?

## Slide 14: Example: Series and Random Amounts
Convert the cash flows shown below (black arrows) into
an equivalent annual worth A in years 1 through 8 (red arrows)
at i = 10% per year.
0 1 2 3 4 5 6 7 8
A = $3000
i = 10%
$1000
0 1 2 3 4 5
A = ?
Solution:
1. Convert all cash flows into P in year 0 and use A/P with n = 8
2. Find F in year 8 and use A/F with n = 8
Solve for F: F = 3000(F/A,10%,5) + 1000(F/P,10%,1)
= 3000(6.1051) + 1000(1.1000)
= $19,415
Find A: A = 19,415(A/F,10%,8)
= 19,415(0.08744)
= $1698
Approaches:

## Slide 15: Shifted Arithmetic Gradients
Shifted gradient begins at a time other than between periods 1 and 2
Present worth PG is located 2 periods before gradient starts
Must use multiple factors to find PT in actual year 0
To find equivalent A series, find PT at actual time 0 and apply (A/P,i,n)

## Slide 16
Example: Shifted Arithmetic Gradient
Solution:
John Deere expects the cost of a tractor part to increase by $5 per year beginning 4 years from now. If the cost in years 1-3 is $60, determine the present worth in year 0 of the cost through year 10 at an interest rate of 12% per year.
0
1
2
3
10
4
5
60
60
60
65
70
95
PT = ?
i = 12%
First find P2 for G = $5 and base amount ($60) in actual year 2
P2 = 60(P/A,12%,8) + 5(P/G,12%,8) = $370.41
Next, move P2 back to year 0
P0 = P2(P/F,12%,2) = $295.29
Next, find PA for the $60 amounts of years 1 and 2
PA = 60(P/A,12%,2) = $101.41
Finally, add P0 and PA to get PT in year 0
PT = P0 + PA = $396.70
G = 5
0 1 2 3 8
Gradient years
Actual years

## Slide 17
Shifted Geometric Gradients
Shifted gradient begins at a time other than between periods 1 and 2
Equation yields Pg for all cash flows (base amount A1 is included)
For negative gradient, change signs on both g values
Pg = A 1{1 - [(1+g)/(1+i)]n/(i-g)}
Equation (i ≠ g):
There are no tables for geometric gradient factors

## Slide 18
Example: Shifted Geometric Gradient
Weirton Steel signed a 5-year contract to purchase water treatment chemicals from a local distributor for $7000 per year. When the contract ends, the cost of the chemicals is expected to increase by 12% per year for the next 8 years. If an initial investment in storage tanks is $35,000, determine the equivalent present worth in year 0 of all of the cash flows at i = 15% per year.

## Slide 19
Example: Shifted Geometric Gradient
Gradient starts between actual years 5 and 6; these are gradient years 1 and 2.
Pg is located in gradient year 0, which is actual year 4
Move Pg and other cash flows to year 0 to calculate PT
PT = 35,000 + 7000(P/A,15%,4) + 49,401(P/F,15%,4) = $83,232
Pg = 7000{1-[(1+0.12)/(1+0.15)]9/(0.15-0.12)} = $49,401

## Slide 20: Negative Shifted Gradients
For negative arithmetic gradients, change sign on G term from + to -
For negative geometric gradients, change signs on both g values
All other procedures are the same as for positive gradients
General equation for determining P: P = present worth of base amount - PG
Pg = A1{1-[(1-g)/(1+i)]n/(i+g)}
Changed from + to -
Changed from + to -
Changed from - to +

## Slide 21
Example: Negative Shifted Arithmetic Gradient
For the cash flows shown, find the future worth in year 7 at i = 10% per year
F = ?
0 1 2 3 4 5 6 7
700
650
500
450
550
600
G = $-50
Gradient G first occurs between actual years 2 and 3; these are gradient years 1 and 2
Solution:
0 1 2 3 4 5 6
Actual years
Gradient years
PG is located in gradient year 0 (actual year 1); base amount of $700 is in gradient years 1-6
PG = 700(P/A,10%,6) – 50(P/G,10%,6) = 700(4.3553) – 50(9.6842) = $2565
F = PG(F/P,10%,6) = 2565(1.7716) = $4544
i = 10%
PG = ?

## Slide 22: Summary of Important Points
P for shifted uniform series is one period ahead of first A;
n is equal to number of A values
F for shifted uniform series is in same period as last A;
n is equal to number of A values
For gradients, first change equal to G or g occurs
between gradient years 1 and 2
For negative arithmetic gradients, change sign on G from + to -
For negative geometric gradients, change sign on g from + to -